Green buildings
1-general principles
-----
Whether you want to obtain local materials or energy independence,
green buildings allow greater resilience.

The use of local and traditional construction materials allows the conservation of construction techniques.

Traditionally, vernacular materials (nearby or at short distances) were used, therefore often inexpensive.

Green buildings make it possible to live in a healthier environment and provide a response to environmental crises.

This type of construction requires more labor, therefore more social intensity by sharing ancestral know-how
or by using modern techniques with ancestral materials.
-----
Green building has several founding principles.

Take into account its environment (climate, vegetation, presence of materials, etc.)
Being in interaction with its environment (capturing heat and light, treating its waste and wastewater locally, recovering rainwater, etc.)
Properly manage the flow of air, water, energy and materials used on a daily basis.
Use healthy and local materials. Avoid composites or transformed materials and favor what can return to the earth without impact.
Have compact habitats, well oriented, insulated and well ventilated (naturally or mechanically).
In the case of dwellings, have good thermal inertia.
Favor less energy-intensive uses (passive, economical, efficient, coupled, recovery of losses, etc.)
-----
The compactness and the sunshine allow a passive economy.

The compactness (c) of a building is its area divided by its volume (S/V).

The smaller the number, the more compact the building. A compact building uses less material and less energy.

Sunshine is maximized by windows where there is the most sun (in the south), intermediate in the east and west, and minimized in the north.

You can also use skylights, light colors and avoid obstacles blocking the light.

The distribution of rooms according to light needs during the day is also important.

It is also necessary to protect yourself from the sun in summer.

-----
Temperature is an important element for well-being and energy reduction.

The perceived temperature integrates the temperature of the air and that of the surrounding walls. The wall covering materials are therefore important.

Good inertia attenuates temperature variations in both summer and winter.

Good insulation minimizes thermal bridges, particularly through EWI (External wall insulation).

Most often a good insulator is a material that contains still air. The range of natural insulators is varied.

Other factors influence thermal comfort, such as ambient air humidity and air velocity.

For comfort, the air should be neither too dry nor too wet. Some insulation or walls regulate humidity.
-----
The materials used have functions and impacts.

Materials have impacts that must be minimized (Energy / transport / recyclability / toxicity on humans and the environment)…

The materials respond to functions (light, removable, transparent, insulating, load-bearing, aesthetic, etc.) that satisfy their uses.

A very wide variety of materials have been used over the centuries to build.

Most often because they were locally available and adapted to the needs.

We can cite the best known such as stone, earth, sand, plants, clay, wood or even straw.

Depending on the times and places, less common things were also used such as shells, bones, skin, fur or dung…

From the base of the house to the roof, each of these materials met a need.

-----
Created under Open License by « de la graine à l’humus »

Find more information on our website:
www.seedtohumus.org

-----
Join us on the site if you want to contribute (translation, design, IT, content, etc.).

There is room for everyone!
-----
Merci à toutes les sources qui ont permis ce projet ouvert !

- Icons : Font Awesome (CC BY 4.0 license).
- Music : Javolenus, Cherish (CC BY NC 3.0 license) | Vinyl Crackle 1, Scottyhigh20 (CC0 license)
- Font : DejaVu sans
- Script, research, editing: Ben
- Proofreading : Mickaël Verger, Botmobil
- Advice: Adèle