How can we decrease our environmental impact?
3-Environmental engineering
-----
With ecological restoration, we have seen how we can act to repair all or part of the damage caused to the environment.
-----
Environmental engineering, on the other hand, aims to minimize or neutralize the environmental impact, or even to have a positive impact.

Thus, environmental engineering is concerned with reducing environmental impact and improving the quality of life.

Sustainable development is one of the goals.

"development that meets the needs of the present without compromising the ability of future generations to meet theirs"

Several "tools" are available to analyze our impact. We will see later what to do following this analysis.
-----
For individuals, the impact is often calculated by the ecological footprint or the carbon footprint.
-----
For services or products, the impact is rather calculated by the carbon footprint or with life cycle analysis.

Let’s elaborate on this a bit…
-----
For individuals, the ecological footprint is the equivalent of the exploited area that is needed to meet our consumption.

This includes housing, food, transport, consumer goods,...

2 global hectares, the unit of measurement used, represents the value for which our children would have access to as many resources as we do.

Currently, the inhabitants of the richest countries exceed this value by 3, 4 or 5 times.

Here are the average values ​​per inhabitant in 2013.
-----
Still for individuals, the other calculation by carbon footprint measures greenhouse gas emissions contributing to global warming.

In the same way it includes housing, food, transport, consumer goods...

This value is generally calculated in kilogram CO2 equivalent (carbon dioxide).

CO2 is the standard value which is equal to 1. By equivalence, the global warming potential of the other gas emissions is determined.

For example, methane (CH4) has a value of 28. Thus 1 kg of methane has a warming potential 28 times higher compared to 1 kg of CO2.

Some gases have very high values ​​such as sulfur hexafluoride (SF6) which is 23,500.

Here are the average per capita carbon footprints for 2017.

Depending on the carbon or ecological footprint measurement, our perception is oriented either on the impact on the Earth or on global warming.
-----
For services or products, the impact is calculated by the carbon footprint or with life cycle analysis.
-----

The carbon footprint is in fact the same approach as the carbon footprint of individuals.

The result of the calculation depends on the limit of the study.

We can seek to have a more global approach by considering all the components of a service and a product
or only a part.
-----
Life Cycle Assessment (or LCA) has a much more comprehensive approach.

For a product, the general steps to consider are raw material acquisition and energy sources; transportation and distribution;
production steps; use of the product; end of life management (recycling, destruction, storage, refurbishing,...);
the manufacture/life/end of life of the required infrastructures for all these stages.

With a more global vision, the Life Cycle Assessment highlights the resources (living or not); climate change ;
the quality of ecosystems; ozone destruction; soil acidification; acidification and eutrophication of rivers or oceans;
smog (urban pollution fog); radioactivity ; land use; toxicology (on humans or the environment).

We'll cover some of the "tools" in more detail in future videos…

-----
Individuals, companies, institutions, communities,…,
everyone can act to reduce its environmental footprint

Find resources at www.seedtohumus.org

-----
Created under Open License by « de la graine à l’humus »

Find more information on our website:
www.seedtohumus.org
-----

Join us on the site if you want to contribute (translation, design, IT, content, etc.).

There is room for everyone!
-----
Thanks to all the sources that made this open project possible!

- Icons : Font Awesome (CC BY 4.0 license), except the molecules
- Music : Javolenus, Cherish (CC BY NC 3.0 license) | Vinyl Crackle 1, Scottyhigh20 (CC0 license)
- Wikipedia FR (Ecological restoration)
- Font : DejaVu sans
- Script, research, editing: Ben
- Advice: Adèle